## Slide 1
HCAS Alert Indicators
Human Collision Avoidance System — A multi-sensory feedback architecture designed to deliver intuitive, direction-aware, and priority-driven alerts through haptic, visual, and audio signals.
FEEDBACK DESIGN SYSTEM

## Slide 2
SENSORY CHANNELS
Three Pillars of Alert Delivery
HCAS fuses three independent sensory channels into a unified feedback system — each encoding a different dimension of situational awareness.
Haptic
Encodes direction and proximity through pulse patterns and vibration intensity on the body.
Visual LED
Encodes severity via color and blink speed — green, yellow, and red at a glance.
Audio
Encodes urgency through tone patterns — single beeps to continuous alarm signals.

## Slide 3
Directional Haptic Language
Direction Mapping
Left Vibration
Hazard detected on the left side
Right Vibration
Hazard detected on the right side
Both Sides
General or frontal danger ahead
Pulse Pattern Language
Short Pulses
Low-level warning — stay alert
Rapid Pulses
Elevated urgency — take action
Continuous Vibration
Critical danger — immediate response required

## Slide 4
PROXIMITY & VISUAL FEEDBACK
Distance-Based Signals + Smart LED Behavior
Smart LED Color System
The LED array communicates hazard severity at a glance, even in peripheral vision:
Blink speed mirrors urgency. Animated light flow indicates hazard direction across the device surface.
🟢 Green
Clear — no immediate threat
🟡 Yellow
Caution — hazard detected nearby
🔴 Red
Critical — collision risk imminent

## Slide 5
INTELLIGENCE LAYER
Adaptive Escalation & Multi-Sensory Fusion
Adaptive Escalation Logic
Alerts begin at minimal intensity and escalate only when risk persists — avoiding unnecessary alarm fatigue while ensuring critical events are never missed.
Stage 3
Stage 2
Stage 1
Why Multi-Sensory Fusion?
Relying on a single channel creates single points of failure — noise blocks audio, bright light washes out LEDs. Fusing all three senses:
Reduces average reaction time
Compensates for environmental interference
Encodes richer situational data simultaneously

## Slide 6
Context-Aware & Motion-Aware Feedback
Moving Toward Hazard
Alert intensity increases dynamically as the user's trajectory converges with the threat — maximizing urgency when it matters most.
Moving Away from Hazard
Alert intensity decreases as the user diverges from the threat, reducing unnecessary feedback and cognitive load.
Temporal Escalation
Alert frequency increases over time if the hazard is unresolved, creating a mounting sense of urgency that drives faster reaction.

## Slide 7
SYSTEM RESILIENCE
Smart Filtering, Silent Mode & Energy Management
1
False Alert Reduction
Transient signals below a persistence threshold are ignored — only sustained threats trigger alerts, cutting unnecessary noise.
2
Silent Mode
Audio alerts are substituted with stronger haptic feedback in noisy or quiet environments — maintaining full effectiveness without sound.
3
Energy-Aware Alerting
When battery is low, brightness, audio, and vibration intensity are reduced. Critical alerts are always preserved and prioritized.

## Slide 8
Priority-Based Alert System
When multiple simultaneous hazards are detected, HCAS presents only the highest-risk alert — preventing sensory overload and keeping feedback clear, focused, and actionable.
Single Alert Rule
Only the dominant threat is surfaced at any moment
No Overload
Competing signals are suppressed to preserve clarity
Actionable Output
Every alert delivered is one the user can immediately act on

## Slide 9
www.Analysion.com