UPDATED AUDIO COMPETENCY TEST
(Modernized Edition)

PART 1 – TRUE / FALSE
Circle True or False
1. A transducer converts energy from one form to another, such as electrical energy into sound.
   True ___ False ___
2. RMS power is a mathematical method of expressing continuous power, not peak output.
   True ___ False ___
3. Intermodulation distortion occurs when two or more frequencies interact to produce new frequencies not present in the original signal.
   True ___ False ___
4. Negative feedback is commonly used in modern amplifier design to reduce distortion and improve stability.
   True ___ False ___
5. A heat sink is used to dissipate excess heat in both solid-state and tube-based equipment.
   True ___ False ___
6. Speaker placement can have a greater effect on sound quality than changing amplifiers.
   True ___ False ___
7. A higher signal-to-noise ratio indicates less background noise relative to the signal.
   True ___ False ___
8. A DAC converts digital data into an analog electrical signal.
   True ___ False ___
9. Bit depth primarily affects dynamic range.
   True ___ False ___
10. Sample rate primarily affects frequency response.
    True ___ False ___
11. Phase issues can affect imaging and bass response without changing frequency response measurements.
    True ___ False ___
12. Room reflections can significantly alter perceived tonal balance.
    True ___ False ___
13. Direct-coupled amplifier outputs eliminate the need for output capacitors.
    True ___ False ___
14. Speaker impedance is constant across all frequencies.
    True ___ False ___
15. A crossover divides frequencies so each driver operates within its optimal range.
    True ___ False ___
16. Jitter refers to timing errors in a digital signal.
    True ___ False ___
17. Class D amplifiers are inherently digital amplifiers.
    True ___ False ___
18. Acoustic treatment reduces sound pressure level in a room.
    True ___ False ___
19. A higher damping factor generally indicates better control of woofer motion.
    True ___ False ___
20. Two amplifiers with identical power ratings can sound different due to circuit design and load interaction.
    True ___ False ___

PART 2 – MULTIPLE CHOICE
Circle the best answer
1. Frequency is measured in:
   a. Decibels
   b. Hertz
   c. Volts
   d. Ohms
2. Dynamic range refers to:
   a. Maximum power output
   b. Difference between loud and soft passages
   c. Speaker efficiency
   d. Frequency extension
3. Intermodulation distortion is best described as:
   a. Harmonic multiples of a single tone
   b. Noise added by tape
   c. New frequencies created by interacting tones
   d. Output clipping
4. The primary function of a preamplifier is to:
   a. Drive speakers directly
   b. Increase current delivery
   c. Select sources and control signal level
   d. Convert digital signals
5. A DAC’s output is typically:
   a. Digital
   b. Optical
   c. Analog
   d. RF
6. Speaker sensitivity is commonly measured as:
   a. Ohms at 1 kHz
   b. dB at 1 watt / 1 meter
   c. RMS power
   d. Cabinet volume
7. Room modes primarily affect:
   a. Treble clarity
   b. Midrange articulation
   c. Low-frequency response
   d. Imaging height
8. Phase misalignment between speakers can result in:
   a. Increased efficiency
   b. Bass cancellation
   c. Lower distortion
   d. Wider bandwidth
9. A higher bit depth allows for:
   a. Higher playback volume
   b. Lower distortion and greater dynamic range
   c. Wider stereo separation
   d. Faster data transfer
10. A crossover slope determines:
    a. Cabinet tuning
    b. How quickly frequencies are attenuated
    c. Driver sensitivity
    d. Amplifier efficiency
11. Impedance is best described as:
    a. Electrical pressure
    b. Electrical flow
    c. Opposition to current flow in AC circuits
    d. Power consumption
12. Slew rate describes:
    a. Maximum amplifier power
    b. How fast an amplifier can respond to changes
    c. Speaker efficiency
    d. Noise rejection
13. Damping factor is a relationship between:
    a. Input and output voltage
    b. Speaker impedance and amplifier output impedance
    c. Signal and noise
    d. Power and efficiency
14. Jitter is most likely to affect:
    a. Frequency balance
    b. Timing and imaging
    c. Output power
    d. Speaker impedance
15. Acoustic absorption primarily reduces:
    a. Reflected sound energy
    b. Direct sound pressure
    c. Bass extension
    d. Speaker sensitivity
16. Class A amplifiers are characterized by:
    a. High efficiency
    b. Switching output devices
    c. Continuous conduction
    d. Digital signal processing
17. A balanced audio connection helps reduce:
    a. Power consumption
    b. Ground loops and noise
    c. Frequency response errors
    d. Speaker distortion
18. The purpose of a subwoofer crossover is to:
    a. Increase volume
    b. Improve imaging
    c. Manage low-frequency distribution
    d. Reduce amplifier heat
19. Clipping occurs when:
    a. Speakers exceed excursion limits
    b. An amplifier runs out of voltage or current
    c. A DAC loses lock
    d. Phase is inverted
20. System gain structure refers to:
    a. Speaker placement
    b. Relative levels between components
    c. Room size
    d. Cabinet tuning
Name;______________________________	Date:_____________

ANSWER KEY WITH EXPLANATIONS
PART 1 – TRUE / FALSE
1. True
   A transducer converts one form of energy into another. Speakers and cartridges are classic examples.
2. True
   RMS describes continuous, usable power, not momentary peaks.
3. True
   IM distortion produces sum and difference tones that were never in the source signal.
4. True
   Negative feedback is widely used to improve linearity, reduce distortion, and control gain.
5. True
   Tube gear uses heat sinks too, sometimes external, sometimes integrated into the chassis.
6. True
   Placement often changes the sound more than swapping electronics.
7. True
   Higher signal-to-noise ratio means less noise relative to the signal.
8. True
   A DAC converts digital data into an analog electrical waveform.
9. True
   Bit depth determines how much dynamic range the system can reproduce.
10. True
    Sample rate defines the upper frequency limit that can be captured.
11. True
    Phase errors can wreck imaging and bass without obvious tonal changes.
12. True
    Reflections alter frequency balance, clarity, and spatial cues.
13. True
    Direct-coupled designs eliminate output capacitors between amp and speaker.
14. False
    Speaker impedance varies with frequency, often dramatically.
15. True
    Crossovers divide the spectrum so each driver does what it does best.
16. True
    Jitter is timing error in digital audio, not noise in the analog sense.
17. False
    Class D amplifiers are switching amplifiers, not digital signal processors.
18. False
    Treatment reduces reflections, not overall sound pressure level.
19. True
    Higher damping factor generally means better woofer control.
20. True
    Power ratings alone never tell the whole story.

PART 2 – MULTIPLE CHOICE
1. b. Hertz
   Frequency is cycles per second.
2. b. Difference between loud and soft passages
   Dynamic range is about contrast, not volume.
3. c. New frequencies created by interacting tones
   That’s the hallmark of IM distortion.
4. c. Select sources and control signal level
   Preamps manage signals, not power.
5. c. Analog
   DACs output analog electrical signals.
6. b. dB at 1 watt / 1 meter
   This tells you how loud a speaker is per watt.
7. c. Low-frequency response
   Room modes dominate the bass.
8. b. Bass cancellation
   Phase issues often show up as weak or uneven bass.
9. b. Lower distortion and greater dynamic range
   More bits, more resolution.
10. b. How quickly frequencies are attenuated
    Slope defines how steeply the crossover rolls off.
11. c. Opposition to current flow in AC circuits
    Impedance is frequency-dependent resistance.
12. b. How fast an amplifier can respond to changes
    Slew rate matters for transients.
13. b. Speaker impedance and amplifier output impedance
    That relationship defines damping factor.
14. b. Timing and imaging
    Jitter blurs spatial information.
15. a. Reflected sound energy
    Absorption tames reflections, not direct sound.
16. c. Continuous conduction
    Class A devices are always on.
17. b. Ground loops and noise
    Balanced lines reject common-mode interference.
18. c. Manage low-frequency distribution
    Crossovers route bass where it belongs.
19. b. An amplifier runs out of voltage or current
    That’s clipping, pure and simple.
20. b. Relative levels between components
    Gain structure keeps noise and distortion under control.

SCORING & INTERPRETATION
0–50%
You understand basic concepts but lack practical integration.
Good starting point. Needs experience.
60–70%
Solid foundational knowledge.
You know more than most casual hobbyists.
75–85%
Strong operational understanding.
Comfortable discussing systems, setup, and tradeoffs.
90%+
You genuinely understand audio systems.
This is the level expected of a specialist, not a salesperson.

OLD TEST
Part 1
1. All audio equipment must have warrantee cards returned for the manufacturer's warrantee to be valid.	True ___ False ___
2. AM suppression is the characteristic of an AM tuner to suppress changes of amplitude to reject noise and interference.	True ___ False ___
3. A baffle is the board in which one or several loudspeakers are mounted.	True ___ False ___
4. A heat sink is used only in transistorized components.	True ___ False ___
5. I.F. stands for intermediate frequency.	True ___ False ___
6. I.M.F stands for power rated at intermodulated high frequencies.	True ___ False ___
7. R. M. S. stands for power derived from the equation rootmean squared.	True ___ False ___
8. The higher the F.M. sensitivity in micro-volts the better.	True ___ False ___
9. Power is rated In Hertz.	True ___ False ___
10. Dynamic mass is the effective mass of the moving parts of a pick-up cartridge.	True ___ False ___
11. A transducer converts energy from one form to another, such as a speaker or pick-up cartridge.	True ___ False ___
12. Rumble is low frequency noise in the F.M. section of a tuner.	True ___ False ___
13. Separation is the distance between loudspeakers in a room.	True ___ False ___
14. In a passive circuit a balance control is a potentiometer.	True ___ False ___
15. The tip of a stylus is called the head.	True ___ False ___
16. Multiplex is a type of filter.	True ___ False ___
17. Music power is the maximum power temporarily available from the power amplifier.	True ___ False ___
18. Air suspension is the same as infinite baffle.	True ___ False ___
19. Flop has to do with transistor failure in the output stage of an amplifier.	True ___ False ___
20. CD's are backward compatible and can be played on BluRay players.	True ___ False ___
21. Most modern elecronics do not use negitve feedback in their amplifier stages.	True ___ False ___
22. Component cosmetics has to do with exterior design of audio equipment.	True ___ False ___
23. C.E.S. is the Association of California Electronics Salesmen.	True ___ False ___
24. Since their obsolecance back in the 1980s reel to reel recorders are no longer considered as a viable music format.	True ___ False ___
25. Mil is one ten thousandths of an inch.	True ___ False ___
26. Class A amplifiers are capable of delivering more power than consumed.	True ___ False ___
27. Higher power amplifiers always have more output devises.	True ___ False ___
28. Bridging amplifiers is not feasible with separate mono amps.	True ___ False ___
29. Slew rate is a measure of an amplifiers speed.	True ___ False ___
30. In the U.S. one channel width in FM amounts to 200 KHZ.	True ___ False ___
31. Modulation of FM transmitter frequency of + or – 75khz Ii mits the channel bandwidth to 150khz.	True ___ False ___
32. Narrow bandwidth selection increases selectivity, but also increases distortion.	True ___ False ___
33. Peak limiting compresses high levels of music above a certain loudness level.	True ___ False ___
34. Linear compression restricts the dynamic range of music through all levels.	True ___ False ___
35. In a PLL circuit a reference signal is fed to a phase detector.	True ___ False ___
36. During FM broadcasting, treble tones are boosted at a rate of 10db/octive for clearer reception.	True ___ False ___
37. Two amplifiers might have the same power output rating, yet produce different output levels. True ___ False ___
38. Direct-coupled output stages allow the amplifier's output transistors to be directly connected to the
speaker terminals.	True ___ False ___
1. A capacitor is basically a switch.	True ___ False ___
2. A speaker system does not produce sound below the resonance frequency of its main driver.	True ___ False ___
3. A 1 1/2" dome tweeter, because of its size has better dispersion than a 3/4" dome tweeter.	True ___ False ___
4. The higher the cabinet resonance the clearer the speakers bass response.	True ___ False ___
5. Paul W. Klipsch was credited with the devolopment of the folded horn loudspeaker.	True ___ False ___
6. A piezo electric tweeter has no moving parts.	True ___ False ___
7. Speakers developed in anechoic chambers are not effected by placement in the listening environment.	True ___ False ___
8. Power handling is a direct ratio speaker cabinet size.	True ___ False ___
9. Direct drive turntables are inherently quieter than belt drive turntables.	True ___ False ___
10. Choice of a phono cartridcle is determined by matching cartridge resonance to tonearm compliance.	True ___ False ___
11. Qikartz crystal oscillators are only found in Direct Drive turntables.	True ___ False ___
12. Straight tonearms are inherently superior designs to "S" shaped tonearms.	True ___ False ___

AUDIO TEST
Part 2

1.	Frequency is
a.	measured in mhz.
b.	measured in dbs.
c.	found to have no overtones.
d.	measured on a V.U. Meter.

2.	I.M. distortion is
a.	related to ratios of original tones.
b.	related to ratios of non linearity in combinations of pure tones
c.	sum and difference of overtones.
d.	not an important consideration in tube designs.

3.	The lowest frequency at which direction of sound can be determined by the human ear is
a.	500 hz.
b.	20 hz.
c.	100 hz.
d.	1000 hz.

4.	Drop out is
a.	caused by a defective head.
b.	the result of under biasing the recording.
c.	the result of over biasing the recording.
d	loss of signal on the tape.

5.	Gauss
a.	invented the transistor.
b.	Is a measure of flux density.
c.	discovered the phenomena of non cleation.
d	is measured in Maxwells per millimeter squared.

6.	Hysteresis loop
a.	is measured in gauss.
b.	is a type of motor mechanism.
c.	principle behind tape cartridge playback.
d.	none of the above.

7.	I.P.S. is
a.	a rate of speed.
b.	a rate of frequency.
c.	a rate of power
d.	intermittent phase shift.

8.	Octive is
a.	is the interval between two frequencies of sound.
b.	the ratio of frequencies of the input to the output,,
c.	electrical energy having a ratio of 27,1.
d.	both "a" & "c".

9.	A.C. is
a.	current with non-changing polarity.
b.	voltage with non-changing polarity.
c.	current with periodically changing polarity.
d.	voltage with periodically changing polarity.

10.	Pink noise
a.	a type of harmonic distortion.
b.	random frequencies uniformly distributed over a specific band witIi.
c.	high frequency noise above 5hz.
d.	eliminated by a graphic equalizer.

11.	In class "8" power amplifier circuits, at rated output, amplifier efficiency runst
a.	80 - 90%
b.	60 - 70%
c.	40 – 50%
d.	less than 30%

12. A "Puise-width-Modulation" amplifier is commonly called al
a.	Class "A" amplifier.
b.	Class "B" amplifier.
c.	Cascade amplifier.
d.	Class "D" amplifier.

13.	Amplifier stability refers to its ability to handle2
a.	high impedance.
b.	reactive loads.
c.	low impedance.
d.	a short circuit.

14. Square wave rise time is
a.	same as slew rate.
b.	not important in a preamp.
c.	can be measured in "nano-seconds".
d.	All of the above.

15.	MOS in MOS FET stands fort
a.	Metal Oxide Semiconductor.
b.	Multiple Output Stage.
c.	Military Overload Specification.
Multiple Output Semiconductor,

16. Negative feed-back ist
a.	a method of controlling amplifier output.
b.	a method of controlling amplifier distortion.
c.	not used in most modern amplifier design.
d.	used to drive power meters or L.E.D.s.

17.	In conventional amplifier designt
a.	voltage gain follows current gain.
b.	voltage gain and current gain occur simultaneously .
c.	voltage gain is out of phase with current gain.
d.	voltage gain precedes current gain.

18.	Voltage	is
a.	electrical pressure
b.	electrical flow.
c.	resistance to electrical flow.
d.	increased in a non conductive environment"

19.	Current is:
a.	electrical pressurea
b.	electrical flowa
c.	resistance to electrical flow.
d.	increased in a non conductive environment.

20.	Impedance is:
a.	electrical pressure.
b.	electrical flow.
c.	resistance to electrical flow.
d.	increased in a non conductive environment.

21.	Ohm's law states:
a.	current equals resistance divided by voltage.
b.	current equals voltage divided by resistance.
c.	current equals voltage time resistance.
d.	current equals voltage minus resistance.

22.	A parametric equalizer:
a.	combines two equalizers in metric form.
b.	has multiple bands at fixed frequencies.
c.	has variable bands with adjustable "Q".
has preassigned amplitude and frequencies.

23	IF (intermediate Frequency):
a.	is a signal produced within the tuner by mixing incoming RF signal with a oscillator	generated signal.
b.	is a temporary signal used to cancel AM noise.
c.	is signal found between FM bands.
d.	is frequencies lagging 180 degrees out of phase with primary broadcast signals.

24.	AM (amplitude modulation):
a.	is modulated signal used to cancel RF interference.
b.	is random noise sampled at various sound levels.
c.	modulation accomplished by varying the instantaneous
d.	amplitude (intensity) of the carrier.

25.	LSI stands for:
a.	lateral switching input.
b.	large scale integrated circuit.
c.	large scale inductance.
d.	last surviving inductor.