## Slide 1: LFR Based Food Serving Waiter
Group 4 Members
Nissan Biswas (021213001)
Syed Shihab Rahman (021213019)
Pallab Paul (021213024)
Mohammad Shiamul Islam Fahim (021213038)
Mushfiqul Alam (021213041)

## Slide 2: Introduction
In modern restaurant automation, robotic systems are being used to improve efficiency and service quality. Our project, LFR-based Food Serving Waiter, is designed to autonomously deliver food to customers using a Line Follower Robot (LFR) mechanism.

## Slide 3: Components
STM32 Microcontroller
DC Motor
IR Sensor
Motor Driver
Jumper Wires
Wheels

## Slide 4: Working Principle
The robot is built using an STM32 microcontroller, IR sensors, and DC motors, ensuring smooth navigation and precise stopping at designated tables. The movement of the robot is controlled using Pulse Width Modulation (PWM), which adjusts the motor speed based on sensor feedback.

## Slide 5: Code Explanation
Sensor Reading
The IR sensors detect the black line and send data to the STM32.
The sensor values determine whether the robot should move straight, turn left, or turn right.
Code
if (left_sensor == BLACK && right_sensor == WHITE) {
turnLeft();
} else if (left_sensor == WHITE && right_sensor == BLACK) {
turnRight();
} else {
moveForward();
}

## Slide 6: Code Explanation
Table Detection and Stopping
When the table marker (or sensor trigger) is detected, the robot stops for 5 seconds.
The HAL_Delay(5000); function is used to pause the movement before continuing.
Code
if (table_sensor == DETECTED) {
stopMotors();
HAL_Delay(5000); // Wait for 5 seconds
moveForward();
}

## Slide 7: Code Explanation
PWM Generation for Motor Control
The STM32 uses PWM to regulate motor speed by changing the duty cycle of the signal. For PWM generation we are using Timer-3, Channel-1,2,3. Channel -1&2 for the Right & Left Motor and Channel-3 for additional Motor.
Code: For PWM start.
HAL_TIM_PWM_Start(&htim3, TIM_CHANNEL_1);
HAL_TIM_PWM_Start(&htim3, TIM_CHANNEL_2);
HAL_TIM_PWM_Start(&htim3, TIM_CHANNEL_3);

## Slide 8: Code Explanation
PWM Generation for Motor Control
For the left and right motor speed control.
Code
TIM3->CCR1 = 27000;
TIM3->CCR2 = 27000;

## Slide 9: Code Explanation
IR Sensor Working
The IR sensors are used to detect the black line on the surface.
Each IR sensor consists of an IR LED and a photodiode. The IR LED emits infrared light, and the photodiode detects the reflection.
A black surface absorbs IR light, giving a low output signal, while a white surface reflects IR light, giving a high output signal.
Code
int rightIRSensorValue = HAL_GPIO_ReadPin(IR_SENSOR_RIGHT_PORT, IR_SENSOR_RIGHT_PIN);
int leftIRSensorValue = HAL_GPIO_ReadPin(IR_SENSOR_LEFT_PORT, IR_SENSOR_LEFT_PIN);
if (rightIRSensorValue == GPIO_PIN_RESET && leftIRSensorValue == GPIO_PIN_RESET) {
rotateMotor(MOTOR_SPEED, MOTOR_SPEED);
}
else if (rightIRSensorValue == GPIO_PIN_SET && leftIRSensorValue == GPIO_PIN_RESET) {
rotateMotor(-MOTOR_SPEED, MOTOR_SPEED);
}

## Slide 10
Code Explanation
IR Sensor & PWM Working
Code: For Additional Motor.
else if (rightIRSensorValue == GPIO_PIN_SET && leftIRSensorValue == GPIO_PIN_SET) {
rotateMotor(0, 0);
HAL_Delay(2000);
TIM3->CCR3=30000;
HAL_Delay(1000); // Let the additional motor work for 10 seconds
TIM3->CCR3=0;
HAL_Delay(2000);

## Slide 11: Code Explanation
Motor Driver (L298N) Working
The L298N motor driver is used to control the speed and direction of the DC motors.
The STM32 microcontroller cannot directly drive DC motors, so the L298N acts as an interface.
It has two input pins (IN1 and IN2 for each motor) that determine the direction of rotation.
Code
For Right motor.
void rotateMotor(int rightMotorSpeed, int leftMotorSpeed) {
// Control the right motor direction
if (rightMotorSpeed > 0) {
// Move forward: IN1 = HIGH, IN2 = LOW
HAL_GPIO_WritePin(RIGHT_MOTOR_IN1_PORT, RIGHT_MOTOR_IN1_PIN, GPIO_PIN_SET);
HAL_GPIO_WritePin(RIGHT_MOTOR_IN2_PORT, RIGHT_MOTOR_IN2_PIN, GPIO_PIN_RESET);
}

## Slide 12: Code Explanation
Motor Driver (L298N) Working
For Right motor.
Code
else if (rightMotorSpeed < 0) {
// Move backward: IN1 = LOW, IN2 = HIGH
HAL_GPIO_WritePin(RIGHT_MOTOR_IN1_PORT, RIGHT_MOTOR_IN1_PIN, GPIO_PIN_RESET);
HAL_GPIO_WritePin(RIGHT_MOTOR_IN2_PORT, RIGHT_MOTOR_IN2_PIN, GPIO_PIN_SET);
} else {
// Stop the motor: IN1 = LOW, IN2 = LOW
HAL_GPIO_WritePin(RIGHT_MOTOR_IN1_PORT, RIGHT_MOTOR_IN1_PIN, GPIO_PIN_RESET);
HAL_GPIO_WritePin(RIGHT_MOTOR_IN2_PORT, RIGHT_MOTOR_IN2_PIN, GPIO_PIN_RESET);}

## Slide 13: Code Explanation
Motor Driver (L298N) Working
For left motor.
Code
// Control the left motor direction
if (leftMotorSpeed > 0) {
// Move forward: IN1 = HIGH, IN2 = LOW
HAL_GPIO_WritePin(LEFT_MOTOR_IN1_PORT, LEFT_MOTOR_IN1_PIN, GPIO_PIN_SET);
HAL_GPIO_WritePin(LEFT_MOTOR_IN2_PORT, LEFT_MOTOR_IN2_PIN, GPIO_PIN_RESET);

## Slide 14: Code Explanation
Motor Driver (L298N) Working
For Left motor.
Code
else if (leftMotorSpeed < 0) {
// Move backward: IN1 = LOW, IN2 = HIGH
HAL_GPIO_WritePin(LEFT_MOTOR_IN1_PORT, LEFT_MOTOR_IN1_PIN, GPIO_PIN_RESET);
HAL_GPIO_WritePin(LEFT_MOTOR_IN2_PORT, LEFT_MOTOR_IN2_PIN, GPIO_PIN_SET);
} else {
// Stop the motor: IN1 = LOW, IN2 = LOW
HAL_GPIO_WritePin(LEFT_MOTOR_IN1_PORT, LEFT_MOTOR_IN1_PIN, GPIO_PIN_RESET);
HAL_GPIO_WritePin(LEFT_MOTOR_IN2_PORT, LEFT_MOTOR_IN2_PIN, GPIO_PIN_RESET);}

## Slide 15: Code Explanation
DC Motor Working
The DC motors control the movement of the robot.
The speed of each motor is adjusted using Pulse Width Modulation (PWM).
Higher PWM duty cycles → Faster motor speed.
Lower PWM duty cycles → Slower motor speed.

## Slide 16: Final Demonstration

## Slide 17: Thank you