## Slide 1
1. All electrical panels should be transparent

## Slide 2
2. All motor should have working status indicator
(fan arrangement)

## Slide 3
3. All lubrication should have high and low level
marking

## Slide 4
4. All pressure gauges (fixed operating range) should
have OK / Not ok zone

## Slide 5
5. All pressure gauge should be of size visible from
3 feet and same pressure gauge should be used
through out the machine

## Slide 6
6. All pressure gauges should be placed 5 feet above
the ground level for better operator visibility.

## Slide 7
7. All bolts should have match mark

## Slide 8
8. All Pneumatic and hydraulic hoses should have
tags on both the ends

## Slide 9
9. Use Proximity switches instead of Limit switches
for better reliability

## Slide 10
10. Arrow mark indication on all pneumatic and
hydraulic hoses to indicate the direction of flow

## Slide 11
11. All Panel cooler should have working status
indicator ( fan arrangement )

## Slide 12
12. Chiller unit or Dryer unit outlet should be insulated
to prevent condensate formation

## Slide 13
13. All lubrication level indicator should be at
visible level

## Slide 14
14. All coolant line should have coolant flow indicator

## Slide 15
15. All panel cooler should be properly routed to the
near by trench

## Slide 16
16. No loose wires or cables – should be properly
routed

## Slide 17
17. All pneumatic and hydraulic hoses should be
properly routed no entangling of hoses

## Slide 18
18. All valves should have open / close indication with
direction of rotation indication

## Slide 19
19. All solenoid coil should be transparent with
indication

## Slide 20
20. All pneumatic hoses should have protection cover
with proper connector at the ends

## Slide 21
21. All guard should have a transparent opening for
easy inspection

## Slide 22
22. All coupling guard should be transparent for easy inspection

## Slide 23
23. All inaccessible area for lubrication should be provided with double sealed bearing.

## Slide 24
24. All Peripherals (hydraulic unit, coolant tank,
Electric panels, etc should be 8 inch from ground level

## Slide 25
25. All Motor should have direction of rotation
identification.

## Slide 26
26. All motors to be provided with cover for dust protection.

## Slide 27
27. All belt guards to have window for inspection

## Slide 28
28. All hoses to be straight and slightly slack

## Slide 29
29. All Electrical Junction box should be transparent with lock type door.

## Slide 30
30. All machines should be provided with a localized guard for coolant splashing and chip arrest

## Slide 31
31.No gap/holes should be present in electric panels

## Slide 32
32. No open holes on coolant and hydraulic tanks

## Slide 33
33. Indication for effective working of conveyor system

## Slide 34
34. Pipe lines / cables should be 8 inch above the
ground level

## Slide 35
35. Localized coolant guard to eliminate forced
deterioration

## Slide 36
36. Bolt should have only 3 thread extended over the
nut

## Slide 37
37. Single lubrication point – Easy to lubricate and
less time to lubricate

## Slide 38
38. V – belt guard with specification and quantity of
belt

## Slide 39
39. Pneumatic hoses routed with rigid pipes and flexible hoses only at the point of usage or movable portion.

## Slide 40
40. Machining centre guard for tail stock to prevent coolant and burr entry.

## Slide 41
41. Pressure gauges at one location – Easy to inspect

## Slide 42
42. Hydraulic power pack – Floor mounted.

## Slide 43
43. Coolant blockage in the machining centre – Cutout
or transparent sheet for easy to inspect.

## Slide 44
44. Float type coolant level indicator – Easy to inspect.

## Slide 45
45. Elimination of sliding door – Reduction of Cycle time

## Slide 46
46. Hydraulic line routed with rigid pipe with flexible
hose at the point of usage or moving portion

## Slide 47
47. FRL unit with maximum and minimum level marking
for Pressure and Lubricant level.

## Slide 48
48. Pneumatic and Hydraulic circuit fixed permanently
on the panel to avoid loss of diagram in the line

## Slide 49
49. Arrow mark with color coding – Reduced MTTR.

## Slide 50
50. Tool changer / Tool holder transparent guard –
easy to inspect

## Slide 51
51. Localized guard for machine – Easy to CLIT

## Slide 52
52. Quick change over – Reduced Setup time.

## Slide 53
53. T bolt for locking – Reduced Setup time

## Slide 54
54. Hole in the seating surface – Reduced cleaning
time.

## Slide 55
55. Coolant tank – Floor mounted

## Slide 56
56. Transparent guard for Gear box – Easy to inspect

## Slide 57
57. Guard for machining centre alone – Elimination of forced deterioration and energy saving.

## Slide 58
58. Dry machining process – Elimination of coolant
circuit and forced deterioration of machine parts

## Slide 59
59. Hydraulic power pack with temperature indicator

## Slide 60
60. Electrical panel with temperature indicator

## Slide 61
61. Proper routing of coolant return line

## Slide 62
62. Quick fix coupling – Easy to remove

## Slide 63
63. Black and Yellow stripes for moving parts –
operator safety

## Slide 64
64. Press – Top Dead Centre

## Slide 65
65. 100 – 150 mm height pads under machines

## Slide 66
66. Transparent guard for limit and Proximity switches

## Slide 67
67. Hydraulic hose – Suitable bending radius

## Slide 68
68. Hydraulic hose routing without twisting of hoses

## Slide 69
69. Proper length selection of Hydraulic hose

## Slide 70
70. Standard Torque level to prevent leakage in bolted
joints

## Slide 71
71. Proper routing of rigid hoses – Elimination of
leakages

## Slide 72
72. Guard for paper band filter – Better quality of
coolant

## Slide 73
73. Hydraulic / coolant tank with oil specification, capacity, due date of change etc.

## Slide 74
74. Mist Collector – Working status indication

## Slide 75
75. Panel cooler fan on the side and not on the top of
panel – Eliminate dust entry

## Slide 76
76. Color coding of air and water lines.

## Slide 77
77. Clamping of hydraulic hoses – Prevent leakage due
to surge pressure

## Slide 78
78. Reciprocating application packing selection –
Leakage prevention

## Slide 79
79. Ply and socket connectors – Easy machine shifting.

## Slide 80
80. Control on Critical Oil levels.