## Slide 1: Precise Pulse integrator
December 2023
Halcyon Circuits/Bryan Nevins

## Slide 2: Contents
Slide | topics | 
3 | Ideal integrator circuit | 
4 | Waveforms with ideal integrator | 
5 | Finite op-amp bandwidth | 
6 | R Parasitic circuit | 
7 | Waveforms with parasitic | 
8 | R divider fix | 
9-10 | Divider fix waveforms | 
11 | Divider parasitic circuit | 
12 | Tuning cap for divider parasitics | 
13 | Ctune waveforms | 
14 | references | 
contents

## Slide 3: Ideal integrator circuit
The opamp has GBW = 1E9 Hz, so the output is nearly ideal.
contents

## Slide 4: Ideal integrator with pulse input has ramp output
Red: integrator input (1:100)
Green: integrator output
input
output
contents

## Slide 5: Finite op-amp bandwidth has minor effect
purple: integrator input (1:100)
Green: ideal integrator (1GHz GBW opamp)
Blue: 10 Mhz bandwidth opamp—15ns delay
input
output
contents

## Slide 6: Chip R has parasitic Capacitance:
contents
Cp3 = Ri3 parasitic capacitance
(pcb pads + resistor terminals)

## Slide 7: Parasitic advances integrator output
With
parasitic
No parasitic
50ns error
Blue: no parasitic, opamp has finite bandwidth
Red: parasitic, opamp has finite bandwidth
parasitic causes 50ns timing error (advance),
relative to no parasitic.
contents

## Slide 8: R Divider fixes Parasitic
Ra4 and Rb4 cancel the effect of Cp4.
The signal due to Cp4 is now common mode
and has no effect on the output.
The divider mid-points (opamp inputs)
have equal signals at any frequency, because the dividers have the same impedance ratio at all frequencies.
Ra5/RB5 = 2000 = Ci5/Cp5
contents

## Slide 9: Waveforms with divider fix
Red: Cpar=50fF
Blue: Cpar=0
Green: Cpar = 50fF with divider fix
Blue & Green are superimposed.
(cpar = 0 and divider fix)
contents
The error of the divider fix circuit is ~0ns
relative to the Cpar = 0 circuit.
Cpar=50fF

## Slide 10: Waveforms with divider fix
Signal | Op amp bandwidth (Hz) | Cpar (fF) | Correction divider | Time Error (ns)
vo_fbw | 1E7 | 0 | No | 0
Vo_par | 1E7 | 50 | No | 49
vo_par_fix | 1E7 | 50 | Yes | ~0.2
Divider fix error ~ 0.2ns!
contents

## Slide 11: Include all parasitics:
Divider resistors have their own parasitic capacitors, Cpa6 and Cpb6.
This means the divider impedance ratio is not constant over frequency.
This can be fixed with an additional capacitor (next slide)
contents

## Slide 12: Tuning Capacitor for divider
Ctune7 causes the divider C ratio to
be 2000:1, the same as the R ratio.
All the parasitics are cancelled.
(waveforms next slide)
contents

## Slide 13: Chip Implementation
contents
On chip
On PCB
Trim Rb7 so that
Ra7/Rb7 = Cp7/Ci7

## Slide 14: Waveforms for Ctune
Vo_Ctune: All parasitics are cancelled. Integrator output same as no parasitic integrator (vo_fbw)
Vo_all_par: Divider parasitics cause glitches
(Cpa6, Cpb6)
contents

## Slide 15: references
C:\bdn\Career_t\github_website\integrator\ | integrator_latest.asc (local)
contents